Model SS75

Industrial Extracting Machine

Operation Manual

Standard:QB/T2324-1997

Taizhou Tongjiang Washing Machinery Factory

Taizhou Tongyang Washing Machinery Co., Ltd.

Jiangsu P.R.China

Preface

Jiangsu Taizhou Tongjiang Washing Machinery Factory, Taizhou Tongyang Washing Machinery Manufacturing Co., Ltd., a diversified enterprise for design, manufacturing, sales, transportation and services,  is specialized in manufacturing the outfits for fabric, washing, dyeing and ironing, Emulsion Chlorine Washing Machine, Soaks Washing Machine and drying machine. It holds the modern workshops, scientific management regulations, advanced equipments and strong production technology power. We emphasis on absorbing the most advanced technology and processing from domestic and abroad. We can assure the first-class quality and good after-sale services. And we have passed the ISO9001 International Quality Management System Certification and 89/392 EEC CE Certification. The products’ sales network has covered all over the world.

Our products must be inspected strictly and performance test before going out of the factory. To ensure the customers’, the users must check the machines timely after they receive them, if any damaged or other problems, please contact our company directly ASAP.

To ensure that the machines are used safely, reliably and durably, the users must look through the details about the Operation Manual before you use the machines.

Contents

1.  Performance Introduction for Industrial Extracting Machine

1-1 Performance Introduction

1-2 Performance Parameter Table

2.  Structure Introduction for Industrial Extracting Machine

3.  Lifting and Installation for Industrial Extracting Machine

3-1 Lifting of Industrial Extracting Machine

3-2 Power Supply

3-3 Installation of Industrial Extracting Machine

4.  Preparation for the operation

- Operation Methods of Industrial Extracting Machine

6.  Maintenance of Industrial Extracting Machine

7.  Bearing List of SS751-754 Industrial Extracting Machine

8.  Installation Drawing for Industrial Extracting Machine

9.  Electricity Principle Drawing of SS751-754 Industrial Extracting Machine

1.  Performance Introduction for Industrial Extracting Machine

1-1 Performance Introduction

Industrial Extracting machine is designed according to the Standard of Natural Textile Industry Ministry. It has the feature of single and reasonable structure, high efficiency, little abrasion, low noise, safety and reliability. It is mainly used for the extracting the fabric, chemical material and emulsion goods. And it is widely used in the area of fabric, dyeing, costume, hotel, hospital, chemical industry and emulsion goods.

  - 2 Performance Parameter Table

| 型号规格 Model | SS752-500 | SS753-600 | SS752-800 | SS751-1000 | SS754-1200 | SWE301- 1500 |
| --- | --- | --- | --- | --- | --- | --- |
| 最大容量(Kg) Max. Capacity | 25 | 45 | 80 | 130 | 220 | 500 |
| 转筒尺寸(mm) Drum Size | φ500*260 | φ600*300 | φ800*340 | φ1000*380 | φ1200*480 | φ1500*600 |
| 转筒转速(r/min) Drum Rotate speed | 1000 | 1000 | 910 | 900 | 750 | 750 |
| 电机功率(Kw) Motor Power | 1.1 | 2.2 | 4 | 5.5 | 7.5 | 12 |
| 电 源 Power Supply | 380V/50Hz/3P |  |  |  |
| 外型尺寸(mm) Overall Dimension | 1000*1000 *650 | 1250*1250 *700 | 1500*1500 *800 | 1800*1800 *900 | 2000*2000 *1020 | 2550*1850*1400 |
| 整机重量（kg） Weight | 220 | 420 | 720 | 1050 | 1500 | 2800 |

2.  Structure Introduction for Industrial Extracting Machine

- The industrial extracting machine is the three-foot suspending type structure, which can avoid the vibration when running because of heavy drum.

- The out frame and rotating drum are made of stainless steel plate, the bottom base, round under pan, bearing base and triangle base are all made of cast iron. The drainpipe is at the bottom of the round under pan.

- The main shaft is finished machining after heat treatment by high-quality carton steel.

- The driving area of SS751-754 industrial extracting machine is driven by the triangle adhesive tape. The motor will drive directly the centrifugal starting wheel and can make the machine drive slowly, then reach gradually the designed rotating speed, that can ensure the machine stable running.

- There is brake opening-closing arm inside of the SS751-754 industrial extracting machine, which has good brake performance. And it can make the machine stopping rotating promptly.

3.  Lifting and Installation for Industrial Extracting Machine

3-1 Lifting for Industrial Extracting Machine

The extracting machine is lifted by fork, and the fork shovel foot shovels the bottom of the round base.

3-2 Power Supply

Power Supply is 380V/3PH    50Hz

Actually, the users must purchase by themselves the QZ73 type comprehensive self-starter for the controlling area of SS751-754 industrial extracting machine. The separate fuse is supplied inside of the controlling circuit of the QZ73 type comprehensive self-starter. But the users must install an outside separate general power controlling switch to prevent from short circuit. Every machine must be connected with a separate branch circuit, and it can’t be connected with the lighting circuit and other equipments.

The machine must be earthed reliably according to the local standard in order to ensure safe operation and the machine’s good running.

3-3 Installation of Extracting Machine

- The extracting machine must be fixed on the firm surface, and must be fastened by 3 bolts.

- The extracting machine must be calibrated by level meter during installation.

- The installation size is as per the groundwork drawing.

4.  Preparation for the operation

1. The operator must know well the structure, performance and operation methods of the machine.

2. Check the drum to see whether there is any tool or other articles which are needed to move away near the machine.

3. Check whether there is anything wrong with the circuit connecting, pressure and wiring connection.

4. Turn the drum for several circles to check the drum rotating.

Trial running the machine after finishing inspecting the above steps to check whether the machine is running normally. Normal operation when the trial running is in a normal condition.

5.  Operation Methods of Industrial Extracting Machine

1.   Put the fabric need to be dewatered inside the drum evenly. Keep the fabric even and never overload.

2. Press the starting button of QZ73 type comprehensive starter to

start the motor.

3. The motor is running for 90 seconds, the speed of the machine can

be inclined to the designed rotating speed and the drain pipe begins to drain greatly.

4. After the machine is running for about 8-10 minutes, the stopping button can be pressed when there is no water from the drain pipe. After 1-2 minutes, brake the opening-closing arm brake slowly and the machine is stopped gradually.

5. After the drum is stopped entirely, then take out of the fabric.

- Never brake the opening-closing when the machine is running normally to prevent from damaging the adhesive tape and other parts.

- Never take out of the fabric from the drum when the drum doesn’t stop completely to avoid the accidents.

6.  Maintenance of Industrial Extracting Machine

Maintain periodically to ensure the machine’s running safely and normally.

  - The machine must be maintained periodically and the lubricant must be entered, and keep maintenance once half a year at least.

  - The nuts must be fastened periodically.

  - Often check the V type adhesive tape to see whether it is loose or tight.

  - Often check the power, wire and earthing wire to see whether they are normal and safety.

  - Keep the machine clean, and remain the good working environment.

  - When the machine doesn’t work for a long time, cut off the power and keep the machine clean and dry.

7.  Bearing List of SS751-754 Industrial Extracting Machine

| 机器规格 Machine Spec. | φ500 | φ600 | φ800 | φ1000 | φ1200 |
| --- | --- | --- | --- | --- | --- |
| 轴承代号 Bearing No. | GB/T292 | GB/T292 | GB/T283 | GB/T283 | GB/T283 |
| 轴承规格 Bearing Spec. | 7209AC | 7310B | NU314 | NU316 | NU417 |
| 轴承数量 Bearing Qty | 1 | 1 | 1 | 1 | 1 |
| 安装部位 Installation Position | 轴承座 Bearing Base |
| 轴承代号 Bearing No. | GB/T276 | GB/T276 | GB/T283 | GB/T283 | GB/T283 |
| 轴承规格 Bearing Spec. | 6209 | 6310 | NU312 | NU315 | NU416 |
| 轴承数量 Bearing Qty. | 1 | 1 | 1 | 1 | 1 |
| 安装部位 Installation Position | 轴承座 Bearing Base |
| 轴承代号 Bearing No. | GB/T301 | GB/T301 | GB/T301 | GB/T301 | GB/T301 |
| 轴承规格 Bearing Spec. | 51208 | 51210 | 51212 | 51312 | 51315 |
| 轴承数量 Bearing Qty. | 1 | 1 | 1 | 1 | 1 |
| 安装部位 Installation Position | 轴承座 Bearing Base |
| 轴承代号 Bearing No. |  | GB/T276 | GB/T276 | GB/T276 | GB/T276 |
| 轴承规格 Bearing Spec. |  | 6212 | 6215 | 6217 | 6218 |
| 轴承数量 Bearing Qty. |  | 2 | 2 | 1 | 2 |
| 安装部位 Installation Position | 起步轮 Starting Wheel |
| 轴承代号 Bearing No. |  |  |  | GB/T276 |  |
| 轴承规格 Bearing Spec. |  |  |  | 6215 |  |
| 轴承数量 Bearing Qty. |  |  |  | 1 |  |
| 安装部位 Installation Position | 起步轮 Starting Wheel |

Industrial Extracting Machine Installation Drawing

Eelctrical Principle Drawing for Extracting machine.